## Slide 1: Planning urban trips for practice periods

## Slide 2: Targeted competency elements Lesson Objective
Gather information about the trip to be taken
Search for information on maps
Perform the calculations necessary for trip planning
Determine the itinerary
Planning trips to be taken in urban environments

## Slide 3: Lesson Contents
Collect data from the dispatcher (teacher).
Locate places and addresses on a traditional paper map or with an electronic tool to get an overview.
Determine elements to anticipate (foreseeable potential problems): space for turns, rush hours, restrictive routes, weather conditions, etc.
Optimally determine the routes to follow during practice periods (directions and landmarks for making turns at the right places).
Determine appropriate stopping places for meals or breaks during the periods.

## Slide 4: Presentation of routes to be analyzed in urban environments for practice purposes

## Slide 5: Based on the geographical location of your service point, the teacher will ask you to fill out a grid to plan the urban route that is in the student workbook.

## Slide 6: You must take into account your type of transportation and its specific characteristics.
height, width, and length of vehicles
the time of year (normal or thaw period)
the number of axles and the total loaded mass of vehicles
the type of cargo (e.g., hazardous materials)
rush hour, construction zones, traffic jams

## Slide 7: You must validate the route and check if you comply with regulations.
transits or transit routes
restrictive roads or restricted routes
the height of viaducts and bridges
the space in the turns you will need to make
tunnels (hazardous materials)

## Slide 8: Necessary Equipment
Traditional maps
Electronic maps
Quebec Trucking Network

## Slide 9: Tips for planning a route in an urban environment
Use landmarks to anticipate route changes

## Slide 10: Landmarks warn you of changes
Count the number of streets before the one you need to take.
Identify the name of the street before the one you need to take.
Identify the name of a business before the street you need to take.
Identify a bridge, a river, or a railway before the street you need to take.
Identify the direction to take using: North, South, East or West for numbered roads, and add left or right as needed.

## Slide 11: Landmarks warn you of changes (continued)
Identify the direction to take for any unnumbered road using left or right (e.g., boulevards, streets, avenues, roads, etc.).
7. Make a drawing of the route changes to take.
8. Write in large letters and space out the writing of the routes to take..
9. You should be able to read your document while driving (clean and legible).
Your teacher demonstrates a simple example to you

## Slide 12
Planned locations for meals or breaks, if applicable | 
Step 1 | Upon leaving the courtyard, , Côte St-Pierre
Step 2 | first intersection for Highway 117 North
Step 3 | First intersection on the left for Highway 50 West
Step 4 | etc.
Step 5 | 
Step 6 | 
Step 7 | 
Step 8 | 
Step 9 | 
Step 10 | 
Step 11 | 
Step12 | 

## Slide 13: Good practice!