## Slide 1
CHAPTER 12
PRESENTATION OF MECHANICAL ELEMENTS

## Slide 2: 1. Coupling devices
Parts covered
➤Fifth wheel fasteners (nuts and bolts)
Check the mounting angles to make sure all parts that fasten the fifth wheel to the vehicle frame are present and securely attached.
On both sides of the road vehicle, facing the fifth wheel
➤Inspect the mounting angle and check for the presence and condition of the nuts and bolts that fasten the fifth wheel to the vehicle frame.
Driving a Heavy Vehicle 369
1.B
When the vehicle
is hitched, there is some movement between a fifth wheel fastener (mounting angle) and the vehicle chassis frame.
1.C
When the vehicle
is hitched, more than 20% of the parts fastening the fifth wheel to the vehicle frame are missing, broken or loose on an anchorage.

## Slide 3: 1. Coupling devices
Driving a Heavy Vehicle 369
1.1
When the vehicle
is hitched, 20% or less of the parts fastening the fifth wheel to the tractor frame are missing, broken or loose on an anchorage.
1.1
When the vehicle
is unhitched, one or more parts fastening the fifth wheel is/are missing, broken or loose.
Parts covered
➤Fifth wheel fasteners (nuts and bolts)
Check the mounting angles to make sure all parts that fasten the fifth wheel to the vehicle frame are present and securely attached.
On both sides of the road vehicle, facing the fifth wheel
➤Inspect the mounting angle and check for the presence and condition of the nuts and bolts that fasten the fifth wheel to the vehicle frame.

## Slide 4: 1. Coupling devices
Driving a Heavy Vehicle 370
1.D
When the vehicle
is hitched, 25% or more of the locking pins of a sliding fifth wheel are missing or inoperative.
Parts covered
➤ The sliding fifth wheel locking pins
Check for the presence and condition of the sliding fifth wheel locking pins.
On both sides of the road vehicle, facing the fifth wheel
➤ Check for the presence of the locking pins.
➤ Make sure the pins* are in locked position.
*The fifth wheel is generally locked by two pins (one on each side), and sometimes more. It is important to check all pins.
Important: The percentage covered by the defect concerns the sum of all pins.

## Slide 5: 1. Coupling devices
Parts covered
Fifth wheel fasteners (nuts and bolts)
Check the mounting angles to make sure all parts that fasten the fifth wheel to the vehicle frame are present and securely attached.
On both sides of the road vehicle, facing the fifth wheel
Inspect the mounting angle and check for the presence and condition of the nuts and bolts that fasten the fifth wheel to the vehicle frame.
Driving a Heavy Vehicle 369
1.1
When the vehicle
is hitched, 20% or less of the parts fastening the fifth wheel to the tractor frame are missing, broken or loose on an anchorage.
1.1
When the vehicle
is unhitched, one or more parts fastening the fifth wheel is/are missing, broken or loose.

## Slide 6
Driving a Heavy Vehicle 000