## Slide 1: Competency 3 Lesson 3.10 Road Vehicle Load And Size Limits Guide

## Slide 2: INTRODUCTION
What are the 2 main objectives in Road Vehicle Load and Size Limits Guide?
Notes: Answer : This regulation’s main purpose is to ensure road user safety and protection of “ Roadways and Bridges”.
Reference :Road Vehicle Load and Size Limits Guide ( Page.1)

## Slide 3: DEFINITIONS
Regarding the wheelbase of a semi-trailer, how is this distance measured?
Notes: Answer : This distance is measured from the Kingpin to the center of the axle on a single axle trailer, center of the axle of a tandem axle trailer and center of the axle of a tridem (tri-axle) trailer.
Reference : Road Vehicle Load and Size Limits Guide Page.2 (Wheelbase)

## Slide 4: DEFINITIONS
What is the meaning of GAWR ?
What is the definition of GAWR ?
Notes: Answer : Meaning GAWR : Gross Axle Weight Rating
Answer : Definition GAWR : The maximum load-carrying capacity of an axle within the meaning of the Motor Vehicle Safety Regulations.
Reference : Road Vehicle Load and Size Limits Guide( Page 3)

## Slide 5
x < y = means that x is less than y
x > y = means x is greater than y
x < y < z = means that y is greater than x and smaller than z
x ≤ y = means that x is less than or equal to y
x ≥ y = means that x is greater than or equal to y
Symbols

## Slide 6: DEFINITIONS
How is the distance of the Overhang (Back Swing) measured?
Notes: Answer : Distance measured from the centre of the single, tandem or tridem (tri-axle) rear axle to the rear end of the vehicle, including the load.
Reference : Road Vehicle Load and Size Limits Guide (Page.3)

## Slide 7: DEFINITIONS
What is the particularity of an equivalent tridem “tri-axle” (group of axles equivalent to a triple axle)?
Notes: Answer : A group of axles is the equivalent of a tridem where it is formed of 3 equally spaced axles, comprising at the front a lowered lift axle,
Reference : Road Vehicle Load and Size Limits Guide (Page.4)

## Slide 8: MAXIMUM AUTHORIZED DIMENSIONS
What is the maximum authorized length of a truck?
What is the maximum authorized length of a tractor with semi-trailer?
What is the maximum authorized length of a double train?
Notes: Answer : Truck : 12,5 M
Tractor semi-trailer : 23 M
Double train : 25 M
Reference : Road Vehicle Load and Size Limits Guide (Pages 5 et 6)

## Slide 9: MAXIMUM AUTHORIZED DIMENSIONS
What is the maximum authorized height of a road vehicle?
Notes: Answer : 4,15 M
Reference : Road Vehicle Load and Size Limits Guide ( Page.8)

## Slide 10: MAXIMUM AUTHORIZED DIMENSIONS
What is the maximum authorized width of a road vehicle?
Notes: Answer : 2,6 M
Reference : Road Vehicle Load and Size Limits Guide (Page.9)

## Slide 11: MAXIMUM AUTHORIZED LOAD BY CLASS OF AXLES
What is the load capacity of an axle which belongs to category B.1 ?
Notes: Answer : 5 500 kg. * Axle capacity may be greater when specified by the road vehicle’s manufacturer. (Up to a maximum of 9 000 kg)
Reference : Road Vehicle Load and Size Limits Guide (Page.12)

## Slide 12: MAXIMUM AUTHORIZED LOAD BY CLASS OF AXLES
The maximum permissible load of an equivalent tridem is reduced compared to the tridem axle )tri-axle).
What is this reduction?
Notes: Answer : The limit is reduced by 1,000 kg in the case of a tridem equivalent.
Reference Road Vehicle Load and Size Limits Guide Page.14 (Note bottom of page)

## Slide 13: Thank You For Your Participation