## Slide 1: Transportation of dangerous goods

## Slide 2
Lesson objective:
Resolve problems stemming form the application of regulations.
Competency 3
Transportation of dangerous goods
Notes: Le transport des marchandises dangereuses relève de la Loi de 1992 sur le transport des marchandises dangereuses. Il s’agit d’une loi fédérale qui nous mène au RÈGLEMENT SUR LE TRANSPORT DES MARCHANDISES DANGEREUSES.
La SAAQ met à la disposition des conducteurs de véhicule lourd un document qui les guide dans les actions et la prise de décisions relatives au transport des matières dangereuses.
Voici une série d’exercices et de mises en situation qui vous familiarisera avec l’utilisation du guide.

## Slide 3: WARNING
Provide information on the Transportation of Dangerous goods regulation of the Ministère des Transports du Québec.
page 5 du guide

## Slide 4: INTRODUCTION
What is the main objective of the Transportation of Dangerous Goods Regulations?
Comply with safety rules related to road transportation of dangerous goods.
page 5 du guide
Notes: –Augmenter la sécurité du public pendant le transport.

## Slide 5: CLASSIFICATION
How many classes of dangerous goods are there ?
9 classes that are subdivided according to the characteristics of the given product.
page 6 du guide

## Slide 6: CLASSIFICATION
Who is responsible for determining the classification of a dangerous goods before allowing a carrier to take possession of it?
The shipper.
page 6 du guide

## Slide 7
Guide, page 6 at 10
9 classes

## Slide 8: DOCUMENTATION
•The shipper must prepare and provide (to the carrier) a shipping document;
•At the time of transport, the carrier must have in their possession a paper document.
page 11 guide

## Slide 9: EXAMPLE OF DOCUMENT
page 12 guide
The paper document may be handwritten or printed

## Slide 10: STORAGE AND LOCATION
•The document must be stored in a pouch to the driver’s door;
•Or remain within reach, either on the seat or in view on the driver’s side.
page 13 guide

## Slide 11: CONTAINERS
Cylinders
Jerricans
Pails
Drums
Barrels
Bottles
page 14 guide
Small container (capacity of 450 liters and less)

## Slide 12: CONTAINERS
Road tanks
Intermediate bulk containers
Portable tanks
page 14 guide
Big container (capacity greater than 450 liters)

## Slide 13: TANK TRUCK
A safety marking ;
A device for monitoring driver behavior, or;
An electronic vehicle stability control system.
page 15 guide
Any tank truck containing dangerous
goods must be equipped with :
(vehicle after August 14th 2006)

## Slide 14: TANK TRUCK
Capacité des compartiments d’une citerne ne doit pas excéder 17000 litres;
Doit être muni de 2 cales de roues;
D’un ou deux extincteurs chimiques de
plus de 40 BC.
page 17 guide
Règle concernant le camion-citerne

## Slide 15
Use the parking brake during the unloading
of liquefied gases;
Place both wheels chocks for unloading;
Ensure that all tank truck valves connected to the container are closed.
page 18 guide
Rules concerning tank truck drivers
The driver must:

## Slide 16: HAZARD INDICATIONS
Labels;
Placards;
Markings and signs.
page 22 guide
Hazard indications must be affixed to the containers.

## Slide 17: HAZARD INDICATION
The shipper is responsible for affixing or having affixed the primary and subsidiary class labels; The carrier must ensure that the labels remain in place during transit.
page 22 guide
Smalls containers

## Slide 18: HAZARD INDICATION
On a side of the container other than the one on which it rests; For a gas cylinder, the label must be on the shoulder or close to it.
page 22 guide
The label must be affixed:

## Slide 19: HAZARDOUS INDICATION
Label(s);
Number UN.
page 23 guide
Proper shipping name:

## Slide 20: HAZARDOUS INDICATION
4 placards;
Number UN.
page 23 guide
Bigs containers

## Slide 21: HAZARDOUS INDICATION
page 24 guide
Bigs containers
Greater than 450
liters but less
than 3000
liters.

## Slide 22: PLACARDING
Apply or remove placards when quantities or types of materials change during transit;
Remove them when they are no longer required.
page 24 guide
The carrier must:

## Slide 23
page 25 guide

## Slide 24: TRAINING
Have received appropriate training ;
Hold a training certificate.
page 27 guide
Requirements:

## Slide 25: TRAINING
The certificate expires 36 months after the date of issue.
page 28 guide
Certificate:

## Slide 26: ACCIDENTAL RELEASE
Local police;
Your employer;
Shipper of goods;
The owner, lessee or charterer of the vehicle, infectious substances: CANUTEC at 613-996-6666;
Catastrophic: CANUTEC
Environmental emergency: 1-866-694-5454
page 30 guide

## Slide 27: ERAP – Emergency repsonse assistance plan
The emergency response
assistance plan - ERAP
page 30 guide

## Slide 28: TUNNELS
Pont-tunnel Louis-Hippolyte-La-Fontaine;
Ville-Marie;
Viger;
Joseph-Samson;
Melocheville
page 31 guide
Tunnel traffic regulations:
Prohibition of passage through the tunnel

## Slide 29: TUNNELS
page 31 guide
What is permitted
Notes: Transports Québec
43. Il est interdit de circuler dans le tunnel Louis-Hippolyte-Lafontaine, dans les tunnels Ville-Marie et Viger à Montréal, dans le tunnel Joseph-Samson à Québec ou dans la partie de la voie d'accès au tunnel de Melocheville qui est parallèle à la voie réservée aux véhicules transportant des matières dangereuses:

## Slide 30: TUNNELS
page 31 guide
What is permitted

## Slide 31: RAIL CROSSING
page 33 guide
The driver carrying placarded dangerous goods must stop the vehicle 5 meters from the rail crossing.

## Slide 32: EXEMPTIONS
page 34 guide
Particularity page 34 at 47 .

## Slide 33: SAFETY STANDARDS AND REGULATIONS
On or in front of th evehicle’s front bumper;
On the outer front end, nor in the bucket or on any part of a utility vehicle.
page 48 guide
No dangerous goods shall be installed:

## Slide 34: CROSS BORDER TRANSPORT
Have a copy of the FMCSA;
Hold a FAST card;
The shipment must comply with TDG regulations;
The carrier must prove that the staff have received appropriate training.
page 50 guide
Transportation to the United States:

## Slide 35: SAFETY AND SECURITY MEASURES
TDG certificate;
Shipping document;
Dangers indicators properly in place;
Knowledge of emergency procedures;
8 hours of rest;
Perform the circle check inspection and check the load securement;
Compliance with load and dimension standards
page 53 guide
Before the beginning:

## Slide 36: SAFETY AND SECURITY MEASURES
Refrain from smoking;
Safe driving and road conditions;
Compliance with speed limits;
Braking distance;
Check load securement and tire condition;
Compliance with driving and rest hours;
Avoid consuming alcohol and drugs
page 53 guide
During the transport:

## Slide 37: SAFETY AND SECURITY MEASURES
Reliable communication system;
Transmission of security documents;
Promote tracking systems;
Distress alert button;
Maintenance of a communication exchange network.
page 55 guide
MEANS OF COMMUNICATION:

## Slide 38: Retour sur la théorie EXERCICE

## Slide 39
Thank you for your attention